## Slide 1
The MAC Sublayer (cont'd) 介质访问控制子层(续)
Chapter 4

## Slide 2: Classification of Networks
REVIEW
by transmission media传输介质:
  Wireless networks / Wired networks

## Slide 3: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 4
Access Point
(AP)
Internet
BSS
BSS: Basic Service Set
基本服务集
802.11 Topologies Infrastructure Basic Service Set

## Slide 5
An Infrastructure Basic Service Set is a BSS with an Access Point (AP).
Infrastructure Basic Service Set
802.11 Topologies Infrastructure Basic Service Set

## Slide 6: Wired and Wireless, What Difference ?
If both A and C sense the channel to be idle at the same time, they send at the same time;
Collision can be detected at sender in Ethernet;
Half-duplex radios in wireless cannot detect collision at sender.
A
B
C
A
B
C
Ethernet LAN
Wireless LAN

## Slide 7: IEEE 802.11 MAC Protocol: CSMA/CA载波监听多点接入/冲突避免
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA – sense(监听) before transmitting
  don’t collide with ongoing transmission by other nodes

## Slide 8: IEEE 802.11 MAC Protocol: CSMA/CA载波监听多点接入/冲突避免
802.11: no collision detection(没有冲突检测)!
  can’t sense all collisions in any case: fading, hidden station
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 9: IEEE 802.11 MAC Protocol: CSMA/CA载波监听多点接入/冲突避免
802.11: no collision detection(没有冲突检测)!
  goal: avoid collisions: CSMA/ C(ollision) A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 10
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden station problem
(隐蔽站问题)
B, A hear each other
B, C hear each other
A, C can not hear each other
Hidden station & exposed station
隐蔽站与暴露站问题
means A, C unaware of their interference at B

## Slide 11
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal fading(信号衰减):
B, A hear each other
B, C hear each other
Hidden station & exposed station
隐蔽站与暴露站问题
A, C can not hear each other interfering at B

## Slide 12
(a) The hidden station problem.
(b) The exposed station problem.
Hidden Station & Exposed Station
隐蔽站与暴露站问题

## Slide 13: The hidden station problem 隐蔽站问题
隐蔽站是指在接收结点的覆盖范围内而在发送结点的覆盖范围外的结点。
隐蔽站因听不到发送结点的发送而可能向同样的接收结点发送数据，造成数据包在接收结点处冲突。
冲突后发送结点要重发冲突的数据包，从而降低了信道的利用率。

## Slide 14: Knowledge Checks
Four stations, A, B, C, and D, are shown. Which of the last two stations do you think is closest to A and why?