## Slide 1
The Medium Access Control (MAC) Sublayer 介质访问控制子层
Chapter 4

## Slide 2: The MAC Sublayer
Broadcast channels: a number of stations that share the same “wire”. If one station sends, all the others get to hear it.
Bus
A
B
C

## Slide 3: Broadcast Networks 广播式网络
Single communication channel that is shared by all the machines on the network
1
2
3
4
5
computer
cable
Frames sent by any machine are received by all others

## Slide 4: Broadcast Networks 广播式网络
Also possible to address a frame to ALL machines (special code in the address field) --- Broadcasting广播
Also possible to address a frame to a SUBSET of machines (group number code in the address field) ---Multicasting组播

## Slide 5: The MAC Sublayer
Problem: if you’re sharing a channel, then two or more stations may decide to start frame transmission at the same time, it will lead to frame collision(碰撞、冲突), which means rubbish on the wire.

## Slide 6: The MAC Sublayer
Medium Access Control: allocates the broadcast channel to one of the competing stations分配广播信道给参与竞争的站点之一。

## Slide 7
IEEE 802 STANDARD FOR LANs
The Medium Access Sublayer (ch 4)
THE CHANNEL ALLOCATION PROBLEM 信道分配问题
MULTIPLE ACCESS PROTOCOLS多路存取访问协议
Wireless LAN 无线局域网
VLANs虚拟局域网

## Slide 8
802.1 ：高层局域网协议Higher Layer LAN Protocols
802.2 ：逻辑链路控制Logical Link Control
802.3 ：以太网Ethernet
802.4 ：令牌总线Token Bus
802.5 ：令牌环Token Ring
802.11：无线局域网Wireless LAN
802.15：无线个域网 Wireless Personal Area Network
802.16：宽带无线接入 Broadband Wireless Access
Institute of Electrical and Electronics Engineers

## Slide 9: The Channel Allocation Problem
Static Allocation静态分配
  FDM /TDM (Frequency/Time Division Multiplexing)
    FDM : Radio/TV broadcasts
    TDM : POTS (Plain Old Telephone System)

## Slide 10: Dynamic Channel Allocation Technologies
Pure ALOHA
Slotted ALOHA
CSMA (Carrier Sense Multiple Access载波侦听, 多路存取协议)
CSMA/CD (ETHERNET以太网)
Switching (Fast ETHERNET)
Token passing (Token Ring )
* ALOHA:夏威夷人问候语，欢迎。

## Slide 11: Pure ALOHA
Each station detects collisions探测冲突 by listening to its own signal.
A collision occurs when a sender doesn't receive the signal that it just sent.
After a collision, sender waits a random amount of time and transmits the same frame again.
This technique is known as backoff退避
Basic Idea(contd.):

## Slide 12: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with probability p until success
randomization – why?
Notes: Here's the setting for slotted Aloha.
Let's assume that all frames are the same size, that time is divided into time slots, and that the length of a time slot is the time needed to transmit a single frame.
Nodes are synchronized; they've got a common clock, and nodes begin a frame transmission only at the start of slot times.
And of course, if two or more nodes transmit in a slot, there are going to be collisions, and these collisions are detected by the senders.
Here's how slotted Aloha operates.
It's really simple.
When a node has a frame to send, it simply transmits that frame in the next slot.
Couldn't be simpler.
If there are no collisions, we've got a success.
However, if there are collisions, a node's going to retransmit that frame in each subsequent slot with probability p until it's successful.
And so here we see the use of randomization.
After a collision, the colliding nodes are going to randomize when they attempt a re-transmission of that message.
And you can see why that has to happen.
If two nodes were to always retransmit their messages in the following slot, they'd collide forever.
With randomization, that's to say, transmitting with probability p, hopefully, only one of these nodes is going to transmit and be successful, and the other will transmit in some later slot.
We'll see that randomization is used in many real-world link layer random access protocols, including Ethernet and Wi-Fi, even though the randomization there is done in a slightly different way, but it was Aloha that first put the word random in random access protocols.

## Slide 13: Carrier Sense, Multiple Access (CSMA)载波侦听、多路存取
We can improve the performance of our simple network greatly if we introduce carrier sensing载波侦听(CS).
With CS, each host listens to the data being transmitted over the cable.
Communication Link

## Slide 14
Carrier Sense, Multiple Access (CSMA)载波侦听、多路存取
Communication Link
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!

## Slide 15: Persistent持续 and Nonpersistent非持续 CSMA
1-persistent CSMA
When a station has data to send, it first listens to the channel to see if anyone else is transmitting at that moment.
  If yes, that means that the channel is busy, the station waits until it becomes idle.
  If not, it transmits a frame.

## Slide 16
Nonpersistent CSMA
Before sending, a station senses the channel.
  If no one else is sending, the station begins doing so itself.
Persistent持续 and Nonpersistent非持续 CSMA

## Slide 17
Nonpersistent CSMA
Before sending, a station senses the channel.
  if the channel is already in use, the station does not continually sense it for the purpose of seizing it immediately upon detecting the end of the previous transmission. Instead, it waits a random period of time and then repeats the algorithm.
Persistent持续 and Nonpersistent非持续 CSMA

## Slide 18
Consequently,
the Non-persistent CSMA algorithm leads to better channel utilization
but longer delays than 1-persistent CSMA.
Persistent持续 and Nonpersistent非持续 CSMA

## Slide 19
p-persistent CSMA
When a station becomes ready to send, it senses the channel. If it is idle,
  it transmits with a probability p.
  With a probability q = 1-p, it defers推迟 until the next slot. If that slot is also idle, it either transmits or defers again, with probabilities p and q.
Persistent CSMA

## Slide 20
A host will only transmit its own frames when it cannot hear any data being transmitted by other hosts.
Is it still possible that a collision occurs?
Carrier Sense, Multiple Access (CSMA)载波侦听、多路存取
Communication Link

## Slide 21
站点1
站点2
距离L
传播时延
t
站点2
发送帧
碰撞
站点1在t＝0时发送帧

## Slide 22
If a collision occurs, the station waits a random amount of time and starts all over again.
Carrier Sense, Multiple Access (CSMA)载波侦听、多路存取
Communication Link

## Slide 23
When a station has data to send, it first listens to the channel.
If the channel is busy, the station waits until it becomes idle.
When the station detects an idle channel, it begins to transmit frame, meanwhile listens to the channel in all time
CSMA/CD 载波侦听多路存取/冲突检测 CSMA with Collision Detection

## Slide 24: CSMA载波侦听、多路存取
REVIEW
Carrier Sense: With carrier sensing, A host will only transmit its own frames when it cannot hear any data being transmitted by other hosts.
Multiple Access: Multiple hosts share a single channel
载波侦听: 每个主机在发送数据之前首先监听信道，只有当信道空闲时才发送数据帧；如果信道忙，暂不发送（退避一个随机的时间），以免发生碰撞；
多路存取: 多个主机共享信道。

## Slide 25
CSMA/CD 载波侦听多路存取/冲突检测 CSMA with Collision Detection
站点1
站点2
距离L
传播时延
t
站点2
发送帧
碰撞
站点1在t＝0时发送帧
站点2
停止发送

## Slide 26
Collision Detection: The station's hardware must listen to the cable while it is transmitting. If what it reads back is different from what it is putting out, it knows that a collision is occurring.
It aborts transmission as soon as it detects a collision rather than finish transmitting it’s frames.
CSMA/CD 载波侦听多路存取/冲突检测 CSMA with Collision Detection

## Slide 27: 例题：某局域网采用CSMA/CD协议实现介质访问控制，数据传输速率为10Mbps，主机A和主机B之间的距离为2000m，信号传播速度是2x108m/s。若主机A和主机B发送数据时发生冲突，则从开始发送数据时刻起，到两台主机均检测到冲突止，最短需经过多长时间？最长需经过多长时间？

## Slide 28: 主机A和主机B之间单项传播时延=2000m/(2x108km/s)=10x10-6s =10μs 两台主机检测到冲突时，最短所需时间： (1) 主机A和主机B同时各发送一个数据帧，信号在信道中间发生冲突后，冲突信号继续向两个方向传播。因此，双方检测到冲突需要1个单向传播时延，即10μs。 因此，两台主机均检测到冲突时，最短需经过10μs。

## Slide 29: (2) 两台主机均检测到冲突时，最长所需时间：主机A先发送一个数据帧，当该数据帧即将到达主机B时，主机B也开始发送一个数据帧。这是主机B将立即检测到冲突，而主机A要检测到冲突，冲突信号还需要从主机B传播到主机A，因此，主机A检测到冲突需要2个单向传播时延，即20μs。因此，两台主机均检测到冲突时，最长需经过20μs。

## Slide 30: CSMA/CD 载波侦听多路存取/冲突检测 CSMA with Collision Detection
Quiz: How long will it take them to realize that there has been a collision?
It depends.
In the worst case it is 2τ, the round-trip propagation time. Why?

## Slide 31
CSMA/CD 载波侦听多路存取/冲突检测 CSMA with Collision Detection
站点1
站点2
距离L
传播时延
t
站点2
发送帧
碰撞
站点1在t＝0时发送帧
站点2
停止发送

## Slide 32: CSMA/CD 载波侦听多路存取/冲突检测
REVIEW
CSMA with Collision Detection
  The host always listens to the cable while it is transmitting data.
  It aborts transmission as soon as it detects a collision
  It tries later again, with a “binary exponential back-off algorithm”
冲突检测:在发送数据的过程中始终监听信道，一旦冲突立即中止发送，退避一个随机时间(二进制指数退避算法)，再重新发送。

## Slide 33: IEEE 802.3: CSMA/CD Bus LAN
The IEEE802.3 standard describes the operation of the MAC sublayer in a bus LAN that uses CSMA/CD.
The CSMA/CD Bus LAN is also widely called Ethernet以太网.

## Slide 34: 二进制指数随机退避算法 Binary exponential back-off algorithm
让发生碰撞的站在停止发送数据后，不是立即再发送数据，而是推迟(退避)一个随机的时间，以减少再次发生碰撞的概率。
确定基本退避时间，一般取为争用期2τ。
定义一个参数k，它等于重传的次数，但不超过10。
即 k = min[重传次数，10]。

## Slide 35: 二进制指数随机退避算法 Binary exponential back-off algorithm
从离散的整数集合[0,1,2,…,2k-1]中随机取出一个数，记为r。重传需要推迟的时间t = r× 2τ 。
设置一个最大重传次数，一般为16次。若重传达16次仍不能成功,则丢弃该数据帧, 并向高层报告

## Slide 36
信道忙？
发送帧
碰撞？
发送完？
发送Jam
N≥16?
Yes
No
No
Yes
发送成功
Yes
发送失败
No
延迟随机时间
No
Yes
发送
碰撞次数N+1


CSMA/CD 载波侦听多路存取/冲突检测 CSMA with Collision Detection

## Slide 37: IEEE 802.3: CSMA/CD Bus LAN
Frame formats. (a) DIX Ethernet,
(b) IEEE 802.3.
DIX: DEC, Intel, Xerox
DEC: DigitalEquipmentCorporation数字设备公司
Xerox: Xerox Corporation施乐公司,
（PARC: Palo Alto Research Center, Inc）
the standard also describes the format of the frames

## Slide 38
Data Length: Ranges from 0-1500.
Ethernet Frames should always be at least 64 bytes.
IEEE 802.3: CSMA/CD Bus LAN

## Slide 39: IEEE 802.3: Minimum Frame Length
The End-to-end propagation delay time tprop=?
Example #1:
Cable length d= 400m,
Data rate R = 10 Mbits/sec,
Propagation speed V= 2x108 m/sec

## Slide 40: IEEE 802.3: Minimum Frame Length
The round-trip propagation delay is, of course, twice the end-to-end delay.
Thus the round trip delay is
With a data rate of
each bit has
duration
Example #1 – cont.

## Slide 41: IEEE 802.3: Minimum Frame Length
The number of bits we can fit into a round-trip propagation delay is
  The minimum frame length is thus 40 bits (5 bytes).
Example #1 – cont.

## Slide 42
the distance which the network spans跨度,
the type of media being used
the number of repeaters中继器 which the signal may have to pass through to reach the furthest part of the LAN.
IEEE 802.3: Minimum Frame Length
The minimum frame size is related to the follows:

## Slide 43: Repeaters中继器
  Run at the Physical Layer
  Connect together one or more Ethernet cable segments of any media type
  Extend the distance over which a signal may travel down a cable
  Provide more flexibility灵活性 in network design

## Slide 44
Two nodes are communicating using CSMA/CD protocol.
Transmission rate is 100 Mbits/sec and frame size is 1500 bytes. The propagation speed is 3*108 m/sec.
Calculate the distance between the nodes such that the
time to transmit the frame = time to recognize that the collision have occurred.
EEE 802.3: Minimum Frame Length
Example # 2

## Slide 45: Ethernet Extension 扩展的局域网
At the Physical Layer
  Hub(集线器)
  Repeater(转发器/中继器)
At the Data Link Layer
  Bridge(网桥)
  Switch(交换机)

## Slide 46: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
Notes: In the case of a switch, it does not have a routing protocol and does not need to communicate with other switches .
Instead, it is able to learn which hosts can be reached through which interface, and the process is as follows:
We have A sending a frame to A prime, and at this point, we'll say the switch has just started up, and its forwarding table is empty .
However, any time the switch receives a frame, it can read the source address and it just learned what interface it can use to reach that source address .
So, from this incoming frame, it's just learned that A is on interface 1 .
But while that information is great for next time it needs to send a frame to A, it doesn't help the switch get the frame to A prime .

## Slide 47: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface
switch table
(initially empty)
A
1
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
frame destination, A’, location unknown:flood
destination A location known:selectively send on just one link
plug and play
Notes: So, let's walk through the rest of our example .
We have A sending a frame to A prime and no entries in the switch's forwarding table so far .
As the frame arrives at the switch, it learns from the source field of the frame and populates A's MAC address and port number in the forwarding table .
Since A prime is not in the forwarding table, it has to fall back to its default behavior and flood the frame out all of the other interfaces .
Since the frame went out all the ports, A prime received it and can respond back .
So, it sends a frame to A via the switch, and the switch already knows what interface A lives on, so it can selectively send it out that port .
And it also just learned what interface A prime is on, so it can populate its switch table accordingly .
Now, any future frames from A to A prime will only need to be sent out the port to A prime and will no longer need to be flooded .
So, that's the basics of how a switch is able to populate its forwarding table without the destinations being configured .

## Slide 48: Virtual LANs (VLANs) 虚拟局域网
Cisco Systems

## Slide 49
虚拟局域网其实只是交换局域网给用户提供的一种服务，而并不是一种新型局域网。
虚拟局域网VLAN 是建立在网络交换技术上的，用软件方式实现的逻辑工作组的划分和管理。
Virtual LANs (VLANs) 虚拟局域网

## Slide 50
虚拟局域网是由一些局域网网段构成的与物理位置无关的逻辑组，而这些网段具有某些共同的需求。每一个VLAN的帧都有一个明确的标识符，指明发送这个帧的工作站是属于哪一个VLAN。

## Slide 51
虚拟局域网的站点不受物理位置的束缚和限制。同一虚拟局域网上的站点可以分布在不同的物理网段上，也可以建立在不同的交换机上。
Virtual LANs (VLANs) 虚拟局域网