## Slide 1: The Application Layer 应用层 DNS, Email,…
Chapter 7

## Slide 2: OSI Model versus TCP/IP
Application
Presentation
Session
Transport
Network
Data Link
Physical
Layer 1
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Telnet
FTP
SMTP
HTTP
UDP
TCP
IP
ARP
ICMP
MAC
LLC
Physical Link
DNS

## Slide 3: DNS – The Domain Name System 域名系统
Instead of using the numeric IP Address of the host, it is possible to use the host name. For example:
    www.google.com
    www.njtech.edu.cn
Translation of host names to IP Addresses is done by nodes called Name Servers域名服务器

## Slide 4: Sending a packet from Argon to Neon

## Slide 5: Sending a packet from Argon to Neon
DNS: The IP address of “neon.tcpip-lab.edu” is 128.143.71.21
ARP: What is the MAC address of 128.143.137.1?
DNS: What is the IP address of “neon.tcpip-lab.edu”?
ARP: The MAC address of 128.143.137.1 is 00:e0:f9:23:a8:20
128.143.71.21 is not on my local network.
Therefore, I need to send the packet to my
default gateway with address 128.143.137.1
frame
128.143.71.21 is on my local network.
Therefore, I can send the packet directly.
ARP: The MAC address of 128.143.71.21 is 00:20:af:03:98:28
ARP: What is the MAC address of 128.143.71.21?
frame

## Slide 6: E-mail
Three major components:
user agents
mail servers
simple mail transfer protocol: SMTP
User Agent
a.k.a. “mail reader”
composing, editing, reading mail messages
e.g., Outlook, iPhone mail client
outgoing, incoming messages stored on server
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 7: E-mail: mail servers
user mailbox
outgoing
message queue
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent
mail servers:
mailbox contains incoming messages for user
message queue of outgoing (to be sent) mail messages
SMTP protocol between mail servers to send email messages
client: sending mail server
“server”: receiving mail server

## Slide 8: Some “Web” Terminology术语
Web page consists of objects, each of which can be stored on different Web servers
Object can be HTML 超文本链接语言file, JPEG image, Java applet, audio file,…
Each object is addressable by a URL (Uniform Resource Locaters通用资源定位器*):
http://www.someschool.edu/someDept/pic.gif
path name
host name
protocol
*URL：识别Internet上的文档或资源的一种标准化方法。

## Slide 9: HTTP (HyperText Transfer Protocol)
Web’s application layer protocol
client/server model
  client: browser that requests, receives, “displays” Web objects
  server: Web server sends objects in response to requests
HTTP 1.0: RFC 1945
HTTP 1.1: RFC 2616
PC running
Explorer
Server
running
Apache Web
server
Mac running
Navigator
HTTP request
HTTP request
HTTP response
HTTP response

## Slide 10: Layers in the Example
Send HTTP Request to neon
Establish a connection to 128.143.71.21 at port 80
Open TCP connection to 128.143.71.21 port 80
Send a datagram (which contains a connection request) to 128.143.71.21
Send IP datagram to 128.143.71.21
Send the datagram to 128.143.137.1
Send Ethernet frame to 00:e0:f9:23:a8:20
Send Ethernet frame to 00:20:af:03:98:28
Send IP data-gram to 128.143.71.21
Send the datagram to 128.143.7.21
Frame is an IP datagram
Frame is an IP datagram
IP datagram is a TCP segment for port 80

## Slide 11: Example Web Page
Harry Potter Movies
As you all know,
the new HP book
will be out in June
and then there will
be a new movie
shortly after that…
“Harry Potter and
the Bathtub Ring”
page.html
hpface.jpg
castle.gif

## Slide 12
Client
Server
The “classic” approach
in HTTP/1.0 is to use one
HTTP request per TCP
connection, serially.
TCP SYN
TCP FIN
page.html
G
TCP SYN
TCP FIN
hpface.jpg
G
TCP SYN
TCP FIN
castle.gif
G

## Slide 13
Client
Server
The “persistent HTTP”
approach can re-use the
same TCP connection for
multiple HTTP transfers,
one after another, serially.
Amortizes TCP overhead,
but maintains TCP state
longer at server.
TCP FIN
Timeout
TCP SYN
page.html
G
hpface.jpg
G
castle.gif
G

## Slide 14: Synthesis: a day in the life of a web request
our journey for the protocol stack is now complete!
  physical, link, network, transport, application
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com
Notes: We're going to put together a cross-section of everything we've learned so far in the class to look at a day in the life of a web request.
We've made it as far down the protocol stack as we're going to go.
The only thing left below layer 2 is the physical layer, which doesn't have protocols per se and is really the domain of physicists and electrical engineers.
But we've looked at application protocols, the transport layer, network and routing protocols, and most recently, the link layer.
So we can now put all the pieces together that are required to execute a web request from beginning to end.
And the goal here is just to tie together everything we've looked at so far into one big picture.
Our scenario is that a student is bringing their laptop and connecting it to the campus network before connecting to a search engine.

## Slide 15: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!
Notes: Remember, the internet is a network of networks, so we have our school campus network connected to an ISP, which in turn is connected to Google's network.
So, our mobile laptop arrives and connects to the campus network.
It requests a webpage, and it can display the search engine's homepage.
But it's not quite that simple,

## Slide 16: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
Notes: as we know.
Before the browser will be able to connect to anything, the device needs an address on the network that it just connected to.
Unlike most campus networks, it will use DHCP to get the address.
The DHCP client is an application running over UDP, so the request will be encapsulated in UDP and then in an IP and then in an Ethernet frame to be forwarded over the network.
Remember, the client doesn't know where the DHCP server is, so it will just broadcast this request.
And when it reaches the server, that frame will be demultiplexed to IP and then to UDP and then up to the DHCP server.

## Slide 17: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
Notes: as we know.
Before the browser will be able to connect to anything, the device needs an address on the network that it just connected to.
Unlike most campus networks, it will use DHCP to get the address.
The DHCP client is an application running over UDP, so the request will be encapsulated in UDP and then in an IP and then in an Ethernet frame to be forwarded over the network.
Remember, the client doesn't know where the DHCP server is, so it will just broadcast this request.
And when it reaches the server, that frame will be demultiplexed to IP and then to UDP and then up to the DHCP server.

## Slide 18
Notes: as we know.
Before the browser will be able to connect to anything, the device needs an address on the network that it just connected to.
Unlike most campus networks, it will use DHCP to get the address.
The DHCP client is an application running over UDP, so the request will be encapsulated in UDP and then in an IP and then in an Ethernet frame to be forwarded over the network.
Remember, the client doesn't know where the DHCP server is, so it will just broadcast this request.
And when it reaches the server, that frame will be demultiplexed to IP and then to UDP and then up to the DHCP server.

## Slide 19: DHCP client-server scenario
DHCP server
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
Broadcast: is there a DHCP server out there?
Notes: In the first step, the arriving client broadcasts a DHCP message that will be received on the interfaces of all of the hosts and routers in the subnet to which it's attaching.
The Discover message basically says, "Hey, is there a DHCP server out there?" This is a form of service discovery. The host knows the service it needs (DHCP), so it sends out a broadcast to discover the server that can provide DHCP service.
DHCP runs over UDP. The client uses port 68, and the server will use port 67. In particular, the server will be listening on a socket associated with UDP port 67 for incoming DHCP messages.
And here are the details of the fields in the DHCP Discover message: the client's source IP address containing the UDP segment that contains the DHCP Discover message is zero because the client doesn't have an IP address yet, and the destination IP address is the IP broadcast address, that is all ones (255.255.255.255), and the UDP destination port number is 67, as we just noted before.
Hopefully, there'll be a DHCP server sitting out there somewhere on the subnet, listening for this service discovery message.
Note also that there's a transaction ID field. It's got a value of 654 here, and this will be used by the client to match any reply to this request.
Here's the second step: any DHCP server that receives this broadcast Discoverer message (and there might be several such servers) can reply with a DHCP offer message.
This message basically says, "Hey, I'm a DHCP server, and here's an IP address that you can use."
If we look at the details of this offer message, we see that it comes from the DHCP server with an IP address of 223.1.2.5, as in our figure earlier, and from port number 67. This offer message is being broadcast to all interfaces on the subnet. The DHCP message contains the IP address that the requesting host can use (that's the (Yiaddr) field) and a lifetime in this case of 3600 seconds, that the address can be used for.
Note that the transaction ID here matches the transaction ID of the initial offer message - that's to say, this is a reply to that message.
A client can receive offers from multiple DHCP servers, and this might occur, for example, if there are multiple routers on that subnet.
Now, the first two steps that we've seen here are actually optional. The way to think of the third step (which could also be the first step if the two optional steps aren't taken) is that the arriving client comes in and says, "Hey, here's an IP address that I want to use"
- maybe that's the IP address that it was told it could use in step two (if that step was executed), or maybe it's an address that it already has, in which case the client is really renewing its use of that address, or perhaps it's an address that the client has used before.
You can see here that this message is also broadcast, and then it contains the IP address that the host is proposing to use, and that there's a new transaction ID and a lifetime as well.
The final message is the ACK message from the DHCP server, saying basically, "Okay, you can use that IP address with this given lifetime."

## Slide 20
Data
datagram
packet
frame

## Slide 21
DHCP discover

## Slide 22: DHCP client-server scenario
DHCP server
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Notes: In the first step, the arriving client broadcasts a DHCP message that will be received on the interfaces of all of the hosts and routers in the subnet to which it's attaching.
The Discover message basically says, "Hey, is there a DHCP server out there?" This is a form of service discovery. The host knows the service it needs (DHCP), so it sends out a broadcast to discover the server that can provide DHCP service.
DHCP runs over UDP. The client uses port 68, and the server will use port 67. In particular, the server will be listening on a socket associated with UDP port 67 for incoming DHCP messages.
And here are the details of the fields in the DHCP Discover message: the client's source IP address containing the UDP segment that contains the DHCP Discover message is zero because the client doesn't have an IP address yet, and the destination IP address is the IP broadcast address, that is all ones (255.255.255.255), and the UDP destination port number is 67, as we just noted before.
Hopefully, there'll be a DHCP server sitting out there somewhere on the subnet, listening for this service discovery message.
Note also that there's a transaction ID field. It's got a value of 654 here, and this will be used by the client to match any reply to this request.
Here's the second step: any DHCP server that receives this broadcast Discoverer message (and there might be several such servers) can reply with a DHCP offer message.
This message basically says, "Hey, I'm a DHCP server, and here's an IP address that you can use."
If we look at the details of this offer message, we see that it comes from the DHCP server with an IP address of 223.1.2.5, as in our figure earlier, and from port number 67. This offer message is being broadcast to all interfaces on the subnet. The DHCP message contains the IP address that the requesting host can use (that's the (Yiaddr) field) and a lifetime in this case of 3600 seconds, that the address can be used for.
Note that the transaction ID here matches the transaction ID of the initial offer message - that's to say, this is a reply to that message.
A client can receive offers from multiple DHCP servers, and this might occur, for example, if there are multiple routers on that subnet.
Now, the first two steps that we've seen here are actually optional. The way to think of the third step (which could also be the first step if the two optional steps aren't taken) is that the arriving client comes in and says, "Hey, here's an IP address that I want to use"
- maybe that's the IP address that it was told it could use in step two (if that step was executed), or maybe it's an address that it already has, in which case the client is really renewing its use of that address, or perhaps it's an address that the client has used before.
You can see here that this message is also broadcast, and then it contains the IP address that the host is proposing to use, and that there's a new transaction ID and a lifetime as well.
The final message is the ACK message from the DHCP server, saying basically, "Okay, you can use that IP address with this given lifetime."

## Slide 23
DHCP offer

## Slide 24: DHCP client-server scenario
DHCP server
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Notes: In the first step, the arriving client broadcasts a DHCP message that will be received on the interfaces of all of the hosts and routers in the subnet to which it's attaching.
The Discover message basically says, "Hey, is there a DHCP server out there?" This is a form of service discovery. The host knows the service it needs (DHCP), so it sends out a broadcast to discover the server that can provide DHCP service.
DHCP runs over UDP. The client uses port 68, and the server will use port 67. In particular, the server will be listening on a socket associated with UDP port 67 for incoming DHCP messages.
And here are the details of the fields in the DHCP Discover message: the client's source IP address containing the UDP segment that contains the DHCP Discover message is zero because the client doesn't have an IP address yet, and the destination IP address is the IP broadcast address, that is all ones (255.255.255.255), and the UDP destination port number is 67, as we just noted before.
Hopefully, there'll be a DHCP server sitting out there somewhere on the subnet, listening for this service discovery message.
Note also that there's a transaction ID field. It's got a value of 654 here, and this will be used by the client to match any reply to this request.
Here's the second step: any DHCP server that receives this broadcast Discoverer message (and there might be several such servers) can reply with a DHCP offer message.
This message basically says, "Hey, I'm a DHCP server, and here's an IP address that you can use."
If we look at the details of this offer message, we see that it comes from the DHCP server with an IP address of 223.1.2.5, as in our figure earlier, and from port number 67. This offer message is being broadcast to all interfaces on the subnet. The DHCP message contains the IP address that the requesting host can use (that's the (Yiaddr) field) and a lifetime in this case of 3600 seconds, that the address can be used for.
Note that the transaction ID here matches the transaction ID of the initial offer message - that's to say, this is a reply to that message.
A client can receive offers from multiple DHCP servers, and this might occur, for example, if there are multiple routers on that subnet.
Now, the first two steps that we've seen here are actually optional. The way to think of the third step (which could also be the first step if the two optional steps aren't taken) is that the arriving client comes in and says, "Hey, here's an IP address that I want to use"
- maybe that's the IP address that it was told it could use in step two (if that step was executed), or maybe it's an address that it already has, in which case the client is really renewing its use of that address, or perhaps it's an address that the client has used before.
You can see here that this message is also broadcast, and then it contains the IP address that the host is proposing to use, and that there's a new transaction ID and a lifetime as well.
The final message is the ACK message from the DHCP server, saying basically, "Okay, you can use that IP address with this given lifetime."

## Slide 25
DHCP request

## Slide 26: DHCP client-server scenario
DHCP server
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
Notes: In the first step, the arriving client broadcasts a DHCP message that will be received on the interfaces of all of the hosts and routers in the subnet to which it's attaching.
The Discover message basically says, "Hey, is there a DHCP server out there?" This is a form of service discovery. The host knows the service it needs (DHCP), so it sends out a broadcast to discover the server that can provide DHCP service.
DHCP runs over UDP. The client uses port 68, and the server will use port 67. In particular, the server will be listening on a socket associated with UDP port 67 for incoming DHCP messages.
And here are the details of the fields in the DHCP Discover message: the client's source IP address containing the UDP segment that contains the DHCP Discover message is zero because the client doesn't have an IP address yet, and the destination IP address is the IP broadcast address, that is all ones (255.255.255.255), and the UDP destination port number is 67, as we just noted before.
Hopefully, there'll be a DHCP server sitting out there somewhere on the subnet, listening for this service discovery message.
Note also that there's a transaction ID field. It's got a value of 654 here, and this will be used by the client to match any reply to this request.
Here's the second step: any DHCP server that receives this broadcast Discoverer message (and there might be several such servers) can reply with a DHCP offer message.
This message basically says, "Hey, I'm a DHCP server, and here's an IP address that you can use."
If we look at the details of this offer message, we see that it comes from the DHCP server with an IP address of 223.1.2.5, as in our figure earlier, and from port number 67. This offer message is being broadcast to all interfaces on the subnet. The DHCP message contains the IP address that the requesting host can use (that's the (Yiaddr) field) and a lifetime in this case of 3600 seconds, that the address can be used for.
Note that the transaction ID here matches the transaction ID of the initial offer message - that's to say, this is a reply to that message.
A client can receive offers from multiple DHCP servers, and this might occur, for example, if there are multiple routers on that subnet.
Now, the first two steps that we've seen here are actually optional. The way to think of the third step (which could also be the first step if the two optional steps aren't taken) is that the arriving client comes in and says, "Hey, here's an IP address that I want to use"
- maybe that's the IP address that it was told it could use in step two (if that step was executed), or maybe it's an address that it already has, in which case the client is really renewing its use of that address, or perhaps it's an address that the client has used before.
You can see here that this message is also broadcast, and then it contains the IP address that the host is proposing to use, and that there's a new transaction ID and a lifetime as well.
The final message is the ACK message from the DHCP server, saying basically, "Okay, you can use that IP address with this given lifetime."

## Slide 27
DHCP ack

## Slide 28: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
Notes: Then the server will create the DHCP ACK, encapsulate it back down through all the layers, and broadcast it over the network once again to the client, where it will be returned to the DHCP application.
Remember that in order to accept this, the client will send out another request for that specific address, and it will be confirmed by the server.
So, there are four parts to this exchange.
At that point, the client will have its address, and it will also have the address of some DNS servers and the gateway router, and maybe some other details of the local network.

## Slide 29: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply
Notes: But we're still not ready to send the application-level request because we need to know what IP address to send that request to.
So, we're going to get ready to send the DNS request.
Again, DNS is an application that runs over UDP over IP over Ethernet, etc.
And so, that request will get encapsulated, and it will get down to the link layer.
And this DNS server is not on the local subnet, so that request needs to go through the gateway router.
While the host knows that it needs to send this to the gateway router, it doesn't have the MAC address for the gateway router.
So before we can go any further, we have to use the Address Resolution Protocol (ARP).
So, our ARP query is broadcast through the network, 'Who has this IP address?' And when the gateway router receives it, it will respond back with its MAC address.
So then, at that point, we have the necessary ARP table entry to send the frame for the DNS request out to the gateway router.

## Slide 30: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Notes: So our next problem is how do we find out what MAC address to use as a destination to a frame? The device knows its own MAC address to use in the source field, and we've talked about how a host can use DNS to find out the IP address that it needs to send the IP packet to. But how does it find the MAC address using the destination field of the layer 2 frame? That relies on a protocol called ARP, the Address Resolution Protocol. And this is another distributed database lookup type function, but instead of mapping from a hostname to an IP address, it maps from an IP address to a MAC address.So every node on a network has to maintain an ARP table or a mapping of the IP address-MAC address pairs that it's aware of. Like most other mappings, there's a TTL after which this entry is considered stale and removed from the table. A common default for this TTL is minutes.

## Slide 31: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)
Notes: Now, let's see how we populate this table. We have Host A, and they want to send a datagram to Host B. We assume that Host A has already found out the IP address for Host B, and now it needs the MAC address. When it looks in its ARP table, it doesn't have a mapping for that IP address. So it will send out a broadcast ARP message.Just like the broadcast address in IP is the all-ones address, the broadcast address in Layer 2 is the all-ones address, represented by all "F"s in hexadecimal. So this Layer 2 message says, "Who has this destination IP address that A is looking for?" Every node on the local network will receive this broadcast message, and whichever one has that address should reply using its own MAC address.

## Slide 32: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)
Notes: The frame has a source MAC address and inside it has a source IP address and a target IP address. Now, Host B receives this message and says, "Oh, that's my IP address!" So it responds back using an ARP response that includes its MAC address. It knows what MAC address to send this back to due to the contents of the original message.
so it has the mapping between its ip address and MAC address

## Slide 33: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500
Notes: Host A can then update its ARP table with the contents of this message, and then it can send out all the frames that it needs to the destination MAC address.

## Slide 34: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply
Notes: But we're still not ready to send the application-level request because we need to know what IP address to send that request to.
So, we're going to get ready to send the DNS request.
Again, DNS is an application that runs over UDP over IP over Ethernet, etc.
And so, that request will get encapsulated, and it will get down to the link layer.
And this DNS server is not on the local subnet, so that request needs to go through the gateway router.
While the host knows that it needs to send this to the gateway router, it doesn't have the MAC address for the gateway router.
So before we can go any further, we have to use the Address Resolution Protocol (ARP).
So, our ARP query is broadcast through the network, 'Who has this IP address?' And when the gateway router receives it, it will respond back with its MAC address.
So then, at that point, we have the necessary ARP table entry to send the frame for the DNS request out to the gateway router.

## Slide 35: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
Notes: In this case, the DNS server is being run by the ISP.
And so, our UDP packet gets to the gateway router and then it can be forwarded over to the ISP's network and through their network to the DNS server.
But remember, for all that to work, the ISP's intra-domain routing protocol must be working in order to distribute the forwarding tables to the routers.
And also, BGP must be working between the campus network and the ISP.
Alright, now that our frame has arrived at the DNS server, it's demultiplexed up through the stack to the DNS application running over UDP.
This will be a recursive resolver.
In this case, it looks like it already has Google's IP address cached.
But if it didn't, it would have to go out through the DNS hierarchy, querying the root and then the TLD servers and then Google's authoritative name server to get that IP address back and send it back to the requesting client.

## Slide 36: A day in the life…TCP connection carrying HTTP
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)
Notes: Now that the client knows what IP address to send the request to, we finally get to the HTTP protocol itself, where the GET request is created.
But before that can be encapsulated, we have to perform the TCP connect.
So, TCP creates the control message, encapsulates it down to the stack, and completes part one of the three-way handshake.
When that reaches the transport layer, TCP will respond to the SYN-ACK and send that back through the network to the client.
Once TCP ACKs the SYN-ACK, the connection is fully established.
Usually, TCP will piggyback the initial data with that ACK, so the GET request can be sent out at this point.

## Slide 39: A day in the life… HTTP request/reply
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
Notes: Now we can look at the HTTP layer finally, and we see the GET request being encapsulated over TCP and sent out.
Keeping in mind, TCP will be employing slow start and congestion management throughout all of this.
So, that message is sent over to the server, which decapsulates it up to the web server application.
And the server can respond back with the reply, which would contain the web page requested, assuming the request is valid.
Then, once that packet gets back to the client and demultiplexed up to the application, it can begin displaying the web page.
Of course, this initial object would only be the base HTML, and any style or graphics or what have you that are referenced in that HTML would have to be retrieved in additional connections.
So, as complicated as this day in the life of a web request process was, we still had to simplify a number of steps along the way.
But hopefully, that's helpful in connecting the dots between all of the layers that we've looked at so far in the class.

## Slide 40: A day in the life… HTTP request/reply
time to
transmit
file
initiate TCP
connection
RTT
request file
RTT
file received
time
time
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)

## Slide 42
An internet consists of LAN1, LAN2, LAN3, LAN4 and LAN5, which are connected by four routers, i.e. R1, R2, R3 and R4, with a subnet mask of 255.255.255.0
Please configure IP address for all routers

## Slide 43
An internet consists of LAN1, LAN2, LAN3, LAN4 and LAN5, which are connected by four routers, i.e. R1, R2, R3 and R4, with a subnet mask of 255.255.255.0
Please configure routing tables for router R2 so that all IP packets can be routed to any destination network. (Do not use the Default route)
destination network | subnet mask | next hop

## Slide 44
If we capture a data frame from the data link layer at LAN3, as shown in the following figure. What are the source IP address and destination IP address in the Packet header (in dotted decimal notation以点分十进制的形式) ? What are the port numbers to indicate the source and destination processes on the host and the Web server respectively?
Frame Data 0000-000F 45 00 01 EF 11 3B 40 00 F8 06 BA 9D C0 A8 01 01 0010-001F C0 A8 05 01 04 FF 00 50 E0 E2 00 FA 7B F9 F8 05 0020-002F 50 18 FA F0 1A C4 00 00 47 45 54 20 2F 72 66 63 0030-003F 2E 68 74 6D 6C 20 48 54 54 50 2F 31 2E 31 0D 0A
Frame Header: Frame Type 0x0800
Destination MAC Address | 00:21:27:21:51:EE
Source MAC Address | 00:15:C5:C1:5E:28

## Slide 45
If we capture a data frame from the data link layer at LAN3, as shown in the following figure. What are the source IP address and destination IP address in the Packet header (in dotted decimal notation以点分十进制的形式) ? What are the port numbers to indicate the source and destination processes on the host and the Web server respectively?
Frame Data 0000-000F 45 00 01 EF 11 3B 40 00 F8 06 BA 9D C0 A8 01 01 0010-001F C0 A8 05 01 04 FF 00 50 E0 E2 00 FA 7B F9 F8 05 0020-002F 50 18 FA F0 1A C4 00 00 47 45 54 20 2F 72 66 63 0030-003F 2E 68 74 6D 6C 20 48 54 54 50 2F 31 2E 31 0D 0A

## Slide 46
An internet consists of LAN1, LAN2, LAN3, LAN4 and LAN5, which are connected by four routers, i.e. R1, R2, R3 and R4, with a subnet mask of 255.255.255.0
Assuming Host 2 is a web server. Using HTTP/1.1 protocol with persistent connections in Non-pipelined mode (HTTP/1.1协议，持续的连接，非流水线方式), and the time for one "HTTP Request-Response" is RTT. The Web page (page.html) contains 5 JPEG images. How many RTT will be needed for the host to get the whole Web page?

## Slide 47: The End!
Thanks for your attention!